## Slide 1
Rotorcraft Modeling & Simulation Part 2
Outline
Review of Rigid Body Dynamics and 6DOF Equations of Motion
  Reference Frames / Notation
  Useful kinematical equations
  Translational and Rotational Dynamics
  Euler Angles / Kinematics
Simple Helicopter Model
  Model structure
  Simple Aero Model
Simulation functions Illustrated via the Simple Helo Model
  Numerical Integration
  Numerical Linearization
  Trim
Rotor Dynamic Model
  Flapping Equations of Motion
  Multi-blade Coordinates
  Rotor Forces and Moments
  Dynamic Inflow
Complete Modular Rotorcraft Simulation Model
  Tail Rotor
  Fuselage and Empennage Aerodynamics
  Engine Dynamics
  Flight Controls
  Integrated Simulation Model
  Other Configurations (tandem rotors, tilt-rotors, compounds, multi-copters)

## Slide 2: Simple Helicopter Model
Initially we will develop simulation methods and principles with a highly simplified rotorcraft model
  6 DOF / 12 State model, no rotor or inflow dynamics
  Aerodynamic forces and moments will be static function of aircraft state and controls using simple models
Will demonstrate basic simulation functionality
  Numerical integration
  Trim
  Linearization
The same functions will be extended to more complex simulation models used later in the course

## Slide 3: Simple Helicopter Model
Based loosely on the Bell 206L3
Properties:
  GW = 4000 lbs
  Two-blade teetering rotor system
  Main rotor radius = 18 ft
  Tail rotor radius = 2.7 ft

## Slide 4: Simple Helo Model Structure
As with all simulations implemented in this class, model is set up in time invariant state variable form:
State vector
Control vector
MATLAB functional call of state equations:
Note we use implicit state space form, but SimpleHelo.m is an explicit state space model. It does not use xdot.
We keep this format for consistency with more complex models used later in the class
[xdot,y] = SimpleHelo(x,u,xdot,constants);
Data structure with rotorcraft constants
x, u, y, xdot are state, control, output, and state derivative vectors respectively

## Slide 5: Simple Helo Model Structure
SimpleHelo.m calls two functions:
  SimpleAero.m – Calculates aerodynamic forces and moments
  EqnMot.m – Calculates 6 DOF equations of motion
EqnMot.m function:
SimpleAero.m function:
x_dot=eqnmot(x,FM,constants);
[FM,y]=SimpleAero(x,u,constants);
Returns state derivative
Inputs are states, force and moment vector, and vehicle constants (it needs mass properties)
Returns total forces and moments at CG, and output vector of users choice (I just set to return specific forces).
Inputs are states, control inputs, and vehicle constants

## Slide 6
6-DOF Rigid Body Equations of Motion (in EqnMot.m)

## Slide 7: Overall Structure of Simple Helo Model
Simple Aero
Equations of Motion

## Slide 8: Aerodynamic Component Models
CG
F
T
H
R

## Slide 9: Resultant Force and Moment Vectors at CG
Local Velocities at Each Component
With wind or induced flow:
Local velocity of component relative to Earth frame:
Will use to include induced flow effects on fuselage and horizontal tail

## Slide 10: Fuselage Aero
Assume a simple force model due to drag forces, from Stevens, Lewis, and Jonson:
Neglect fuselage aerodynamic moments. Allows for moments due to distance from fuselage aero center to CG (which is set to 0 in this sim)

## Slide 11: Main Rotor Model
Assumptions:
  Teetering rotor system (no hub moment)
  Small flapping angles
  “Actuator Disk” model: use simplified model to compute total thrust and torque of the main rotor
  No flapping or inflow dynamics
  Zero shaft incidence (Main Rotor Hub Frame is parallel to body frame)
R
G

## Slide 12: Main Rotor Model
Local velocity of main rotor hub:
In-plane and perpendicular components expressed as non-dimensional advance ratios:
Inflow and Main rotor wake skew

## Slide 13: Main Rotor Model
Rotor flapping and rotor forces:
Resultant Forces and Moments due to the main rotor at the CG
Solved through iteration

## Slide 14: Tail Rotor Model
Same model as main rotor, but assume no flapping
Tail rotor frame is rotated 90 deg relative to body frame. Resulting coordinate transformation:
Local velocities in-plane and vertical velocities at tail rotor:

## Slide 15: Tail Rotor Model
Tail rotor thrust and torque, similar to main rotor but simplified (e.g. no cyclic pitch):
Resulting forces and moments due to tail rotor at CG:

## Slide 16: Horizontal Stabilizer Model
Assumptions:
  Lift and drag forces only (no moments or side force)
  No incidence (HT frame is parallel to body frame)
Local velocity at horizontal stabilizer:
Angle of attack and local dynamic pressure:

## Slide 17: Horizontal Stabilizer Model
Consider only lift forces, lift coefficient linear with angle of attack but limited to +/- 1.0
Resultant forces and moments due to horizontal tail at aircraft CG

## Slide 18: Aero Interference Effects
Downwash velocities on fuselage and horizontal tail due to main rotor:
c
“A”