## Slide 1
Rotorcraft Modeling & Simulation Part 3
Outline
Review of Rigid Body Dynamics and 6DOF Equations of Motion
  Reference Frames / Notation
  Useful kinematical equations
  Translational and Rotational Dynamics
  Euler Angles / Kinematics
Simple Helicopter Model
  Model structure
  Simple Aero Model
Simulation functions Illustrated via the Simple Helo Model
  Numerical Integration
  Numerical Linearization
  Trim
Rotor Dynamic Model
  Flapping Equations of Motion
  Multi-blade Coordinates
  Rotor Forces and Moments
  Dynamic Inflow
Complete Modular Rotorcraft Simulation Model
  Tail Rotor
  Fuselage and Empennage Aerodynamics
  Engine Dynamics
  Flight Controls
  Integrated Simulation Model
  Other Configurations (tandem rotors, tilt-rotors, compounds, multi-copters)

## Slide 2: Integration of the State Equations
Numerical solution of the state equations given initial conditions and prescribed control inputs:
State variable equations in explicit form can readily be solved using various time marching methods (see Stevens, Lewis, and Johnson chapter 3.4) – will not cover in this class
  Runge-Kutta Methods
  Linear Multistep Methods
In implicit form, numerical integration requires iteration at each step to resolve implicit state equations (e.g. fixed-point iteration)
MATLAB / SIMULINK offer numerous solvers. SIMULINK is convenient as it is already set up for state equations with input signals, and it can handle “algebraic loops” which occur in implicit state eqns.

## Slide 3: Setup of Rotorcraft State Equations in Numerical Simulations
Aircraft Dynamics

## Slide 4: Integration of State Equations
For engineering analysis would typically use numerical solutions to analyze response to certain “canned” test inputs:
  Step Input
  Pulse Input
  Doublet
  2-3-1-1
Normally want to start the simulation from an equilibrium condition (trim) in order to isolate the effect of the input (as opposed to the effect of initial conditions)
Unstable responses are common in rotorcraft, need to constrain length of time history to have useful data when simulating unstable systems.

## Slide 5: Trim (Equilibrium Computation)
Given State Space System of the form:
Trim seeks to solve for states and controls (trim variables) to meet a set of constraints on the state derivatives and output variables (trim targets), and becomes a problem of solving a system of non-linear equations:
Normally only need to solve subset of the trim variable vector, to meet constraints on a subset of the trim targets.
Typically, the number of trim variables will equal the number of trim targets. But in some cases, there may be additional trim variables, in which case trim might becomes an optimization problem.

## Slide 6: Trim (Equilibrium Computation)
The trimmer.m routine uses a Newton-Raphson method:
The constants structure defines the trim variables and the trim targets via the index arrays TRIMVAR and TRIMTARG:

## Slide 7: Trim (Equilibrium Computation)
The Jacobian is calculated via the numerical linearization scheme. It extracts a sub-matrix from the linear model matrices:
The constants structure also specifies the tolerances used in trim, and a vector of scale factors so that errors in each state are of comparable magnitude.
Constants structure also specifies perturbation sizes used in numerical linearization.

## Slide 8: Numerical Linearization
Extracts linear models in two different forms:
The state equation matrices are related by:
Linearize.m applies a simple centered different scheme with user specified perturbations:
and
C and D matrix computations are similar, but M matrix is as follows:

## Slide 9: Numerical Linearization
Constants structure defines perturbation sizes:
  DELXLIN defines perturbations for states and state derivatives
  DELULIN defines perturbations for controls
Need to be conscious of units when defining perturbation sizes. E.g. do not use perturbation of O(1) when the unit is radians.
Resulting linear model matrices are then usable in LTI objects with the various tools in MATLAB control systems toolbox.

## Slide 10: Numerical Linearization
Linearize.m does not bother constructing a C matrix with the states as output.
Please remember, if you are just interested in state outputs, you can always easily construct such a linear system by setting C to identity (or some submatrix of identity) and D as a zeros matrix.