## Slide 1
Rotorcraft Dynamic Model Part 1
Outline
Review of Rigid Body Dynamics and 6DOF Equations of Motion
  Reference Frames / Notation
  Useful kinematical equations
  Translational and Rotational Dynamics
  Euler Angles / Kinematics
Simple Helicopter Model
  Model structure
  Simple Aero Model
Simulation functions Illustrated via the Simple Helo Model
  Numerical Integration
  Numerical Linearization
  Trim
Rotor Dynamic Model
  Flapping Equations of Motion
  Multi-blade Coordinates
  Rotor Forces and Moments
  Dynamic Inflow
Complete Modular Rotorcraft Simulation Model
  Tail Rotor
  Fuselage and Empennage Aerodynamics
  Engine Dynamics
  Flight Controls
  Integrated Simulation Model
  Other Configurations (tandem rotors, tilt-rotors, compounds, multi-copters)

## Slide 2: State Variable Representation of Rotorcraft Dynamics
State Vector
Control Vector
Fuselage body states
Rotor states
Inflow states
Propulsion system states
Lateral cyclic
Long. cyclic
Collective
Tail rotor collective
Engine throttle
Results in large set of coupled differential equations (state equations):
Includes 6-DOF rigid body equations of motion, rotor flapping and lagging dynamics, finite state dynamic inflow, propulsion system model, and model of aerodynamic effects (typically in tabular form).

## Slide 3: Rotorcraft Simulation Architecture

## Slide 4: The Blade Element Rotor Model
Divide rotor blade into segments along span
  Often desirable to have more segments near tip (equal annular area distribution of blade elements)
Define properties at each segment
  Mass and inertia distribution
  Aerodynamic properties
    Airfoil lift and drag tables as function of a and Mach number
    Moment coefficient needed if modeling flexibile blades
    Airfoil might vary along the span
  Geometric properties
    Chord (may vary along span)
    Sweep (sometimes blade tips are swept)
    Blade twist (variation of pitch along span)
    Location of flapping and lagging hinges
    Flap / lag / pitch coupling in hinges (d3 and a1)
    Geometry of lag damper
  Structural properties
    Force characteristics of lag damper
    Stiffness and damping properties of elastomeric elements
    Structural properties of blade if modeling flexible blades

## Slide 5: The Blade Element Rotor Model
Dynamic model determines motion of rotor blades and the aircraft
Inflow model determines induced air velocities at blade elements
Calculate local air velocity of blade elements and determine blade airloads
Airloads used to calculate blade and vehicle motion
Solution of dynamics, inflow, and air loads are coupled and solved simultaneously in state variable model
Flap Hinge
Lag Hinge
Lag Damper
Blade Element Aerodynamic Control Points

## Slide 6: Rotor Flapping Dynamics
Rigid Rotor System?
R
r
Blade Element
No dynamics associated with rotor system (except possibly inflow dynamics)
All aerodynamic forces on blades are translated to shear forces and bending moments acting on the hub, which translate to forces and moments about the aircraft CG
Rotor model governed by algebraic equations, numerical integration of loads across blade.

## Slide 7
Rotor Flapping Dynamics
In reality all rotor blades will deflect or deform under aerodynamic and inertial loading:
  Deflections out of the plane of rotation (flapping)
  Deflections within the plane of rotations (lagging)
  Deflections about the spanwise axis of blade (blade pitch / feathering / torsion)
Most rotor blades on full-scale aircraft are designed to allow significant flapping and lagging motion using either hinges (articulated rotor system) or flexible elements near the root of the blade (hingeless rotor systems).
Feedom to flap and lag alleviates loads, saves structural weight.
Freedom to flap can alleviate response to turbulence / wind gusts, and in some ways is better for stability and control.
Blade pitch variation is needed for control, blade pitch is governed by the control system.
Rigid blade approximation only good for small scale aircraft / propellers.

## Slide 8: Rotor Flapping Dynamics Flapping Models
Blade
Hub
Hinge
eR
b
Elastic Blade Model
Very accurate model for articulated and hingeless rotors
Requires finite element model of blade structure
Blade
Hub
Hinge Offset Model
Accurate model for articulated rotors
Good approximation of hingeless rotors that are not exceptionally stiff (use equvalent hinge offset)
b
Center Spring Model
Blade stiffness and hinge offset modeled as equivalent flapping spring
No particular accurate, but good tool for teaching basic concepts

## Slide 9
xg
yg
zg
CG
ze
xe
ye
Earth-Fixed or Inertial Frame, Fe
Fuselage-Fixed or Body Frame, Fg
Hub Frame, Fh
xh
yh
zh
gs
Shaft Tilt
xb
yb
zb
Blade Frame, Fb
Reference Frames / Coordinate Systems
W
b
za
xa
ya
Frame of local airmass, Fa
Representative Blade Element

## Slide 10
gs
H
hR
xR
Transformations to Hub System
G
Body to hub transformation. Uses left-handed rotation about y-body axis by shaft incidence angle gS.
Can derive angular velocity vector and velocity of hub in the hub coordinate system.

## Slide 11
xh
zh
y
b
H
F
xb
zb
yb
B
H = Hub Reference Point
F = Flapping Hinge
B = Blade Element
G = Center of Gravity (Body Reference Point)
yh
Rotor Shaft
Blade
Forward
y = 180°
xg
zg
yg
G
Aft
y = 0°
Left
y = 270°
Right
y = 90°
Transformations to Blade System
y =blade azimuth angle
b = blade flapping angle
W = rotor speed
xf
zf
yf
Fh =Non-rotating hub frame
Ff = Rotating hub frame

## Slide 12
Transformations to Blade System
H
F
B
b
eR
(1-e)R
r-eR
Rotate by 180° - azimuth about shaft (z-axis of hub system). Then rotate by flapping angle about flapping hinge (y-axis of rotating hub system)

## Slide 13
Velocities at Blade Element

## Slide 14
H
b
Derivation of Flapping Dynamics
Flapping Spring
Apply Newton’s law, sum flapping moments about the flapping hinge. Use D’Alembert’s form with sum of external and inertial forces:
B

## Slide 15
Derivation of Flapping Dynamics
Define 1st mass moment and 2nd mass moment (moment of inertia) of blade about the flapping hinge as well as weight and CG location
Coriolis Accel Angular Accel of the hub
Flapping Accel. Acceleration of the hub
Centripetal Accel

## Slide 16
Derivation of Flapping Dynamics
Final non-linear flapping equation of motion:

## Slide 17
Aerodynamic Loads on Blade Element
q
f
a
zb
yb
Plane perpendicular to shaft axis (zh)
B,A
f

## Slide 18: Rotor Inflow
Download + Weight
Thrust
Induced Velocities in Plane of the Rotor
Affects angle of attack at local blade section
Varies as function of radius, azimuth, and time
Dynamic inflow theory provides efficient state space equations to model inflow

## Slide 19
Dynamic Inflow
Inflow varies linearly over rotor disk
R
Generalized Dynamic Inflow Model:
Where the coefficients can be driven by state equations based on the theory of Peters and He:
Simplest form is the Pitt-Peters Model (3 state inflow model):
Radial Expansion Functions
Harmonic Expansion Functions
Peters-He inflow model can be scaled to include any number of states

## Slide 20
Local Aerodynamic Velocities at Blade Section
Might also have correction for “skewed flow”, due to radial component.

## Slide 21
Nonlinear Blade Element Model
cl
a
cd
a
M = 0.5
M = 0.9
Linear lift region:
For non-linear simulation will typically use 2D look up tables for Mach number from 0 to 1, and angle-of-attack through 360 degrees

## Slide 22
Simplified Equations
Assumptions
Drop the term related to linear acceleration of the hub:
Drop the blade weight term
Assume small angles for b, f, q, and a. (blade flapping, incidence angle, blade pitch, and blade angle of attack).
Neglect radial flow effects.
Simplify blade section aerodynamic properties: linear lift, constant drag coefficient (will add term that accounts for increased profile drag with a later).
Drop small terms in aerodynamic loads.
Assume W >> rh or W - rh = W
Assume lift forces are much larger than drag
Assume linear lift variation with angle-of-attack:
Not necessary for non-linear simulations on modern computers, but useful for understanding important terms

## Slide 23
Simplified Equations
Non-dimensional system:
Approximations:
Simplified, non-dimensional flapping dynamics:

## Slide 24
Important Non-dimensional Parameters
Flapping frequency ratio = ratio of blade flapping natural frequency relative to rotor speed.
Typically, 1 to 1.1 for conventional rotors (articulated or conventional hingeless).
For stiff rotors, used in Coaxial Lift Offset rotor systems (XH-59A, X-2, SB>1) can be higher, 1.3 to 1.7
Lock number = ratio of aerodynamic forces relative to inertial forces on blade flapping dynamics
Typical range: 3 to 12. Typical value is 8. Heavy, thin blades will tend to have lower Lock number. Lighter wide blades have higher Lock number. Note that the inertia parameter, Ib, tends to scale by R5, so the Lock number tends to scale by c/R.

## Slide 25: Hinge offset model of hingeless rotors
UH-60
Articulated rotor, actual hinge offset = 0.047R.
Flapping frequency ratio = 1.037
BK-117
Hingless rotor system
Flapping frequency ratio = 1.08
Equivalent hinge offset = 0.11R
BO-105
Hingeless rotor system
Flapping frequency ratio = 1.1
Equivalent hinge offset = 0.14R
Blade
Hub
Hinge Offset Approximation of the Blade Deflection

## Slide 26
Simplification and Analytical Integration of Aerodynamic Loads
Hub-Wind Axis Transformation:
VH/a
uh
vh
yw
y
yhw
Forward
Aft
Blade
Will transform all states and controls to hub-wind axes. Solve the flapping response and rotor forces in hub-wind axes, then transform back into the hub frame and then the body frame.

## Slide 27
Simplification and Analytical Integration of Aerodynamic Loads
Drop high order terms, perform integrations:
Inertia Damping Spring Gyroscopic Effects
Aerodynamic Forcing Terms