## Slide 1
Rotorcraft Dynamic Model Part 3
Outline
Review of Rigid Body Dynamics and 6DOF Equations of Motion
  Reference Frames / Notation
  Useful kinematical equations
  Translational and Rotational Dynamics
  Euler Angles / Kinematics
Simple Helicopter Model
  Model structure
  Simple Aero Model
Simulation functions Illustrated via the Simple Helo Model
  Numerical Integration
  Numerical Linearization
  Trim
Rotor Dynamic Model
  Flapping Equations of Motion
  Multi-blade Coordinates
  Rotor Forces and Moments
  Dynamic Inflow
Complete Modular Rotorcraft Simulation Model
  Tail Rotor
  Fuselage and Empennage Aerodynamics
  Engine Dynamics
  Flight Controls
  Integrated Simulation Model
  Other Configurations (tandem rotors, tilt-rotors, compounds, multi-copters)

## Slide 2
xh
zh
y
b
H
F
xb
zb
yb
B
H = Hub Reference Point
F = Flapping Hinge
B = Blade Element
G = Center of Gravity (Body Reference Point)
yh
Rotor Shaft
Blade
Forward
y = 180°
xg
zg
yg
G
Aft
y = 0°
Left
y = 270°
Right
y = 90°
Reference Frames
y =blade azimuth angle
b = blade flapping angle
W = rotor speed
xf
zf
yf

## Slide 3
zh
yi
bi
H
yh
xf
zf
yf
Rotor Forces and Moments
Aft
y = 0°
F
Ultimately need total rotor forces and moments resolved at center of hub, H
Start by finding forces and moments from each blade resolved at the flapping hinge, F
The flapping hinge resides in a rotating frame relative to the hub frame
Will derive based on 4-bladed rotor
eR

## Slide 4: Rotor Forces and Moments
Forces and moments at hub are simply a summation of blade forces with coordinate transformation based on rotor azimuth
Will neglect effect of blade torsion (effects on flight dynamics are smaller than other components)
Moment about flap hinge is due to flap spring. If no flap spring this component is 0 (no moment is transferred about the axis of a hinge)

## Slide 5: Rotor Forces and Moments
Aerodynamic and inertial forces at a representative blade element must be computed and then integrated across the blade to get resulting force and moment at flapping hinge.
These forces can be partitioned into the inertial and aero terms:
Inertial forces can be derived by computing the acceleration at a representative blade element using kinematical relationships.
Aero forces are calculated by computing lift and drag forces at each blade element and resolving into blade frame. Will neglect radial (spanwise) aerodynamic forces.

## Slide 6: Rotor Forces and Moments
Inertial forces require computation of acceleration vector at blade element:
Expressions get quite complex (will not show here).
Integration includes mass distribution. Can make use of blade mass properties:
Will also define two terms wx and wy. These are the angular rates of the hub expressed in the rotating hub coordinate system:
Blade mass
1st mass moment about flapping hinge
2nd mass moment about flapping hinge

## Slide 7: Rotor Forces and Moments
Shear forces at flapping hinge due to inertial forces:
In-plane moment (torque) at flapping hinge due to inertial forces:
As mentioned before, neglect torsion moment Mx and flapping moment My has to be reacted by the flapping spring (if there is one)

## Slide 8: Rotor Forces and Moments
We can simplify by:
  Factoring out W2R to get non-dimensional expressions
  Apply small angle assumptions
  Remove products of non-dimensional terms that are << 1
  Assume rotor speed is much larger than yaw rate:

## Slide 9: Rotor Forces and Moments
Aerodynamic forces – make use of small angle approximations, neglect radial aero forces, assume linear lift / constant drag coefficients (similar to what was done in flapping dynamics):
Can further simplify solution of the integral (without much loss in accuracy) by integrating from the hub center to the tip. Will use the following non-dimensional force parameters (as used in Padfield text):

## Slide 10: Rotor Forces and Moments
The velocity of a blade element relative to the air is given by:
Where vi(r,y) is the local induced downwash.
Can apply hub-wind axis transformation on velocities, flapping angles, controls, and angular rates:

## Slide 11: Rotor Forces and Moments
Non-dimensional tangential and normal velocity (can neglect radial component
Assume 1st harmonic variation on flapping and inflow (use hub-wind axes):
1st derivative of flapping (apply product rule of differentiation):
Apply small angle assumptions:

## Slide 12: Rotor Forces and Moments
Further assumptions: neglect hinge offset in aero terms, and neglect yaw rate term
For brevity, drop “hw” subscript from azimuth angle
Normal aero force, F(1), for blade i is evaluated as:
Can drop numerous second order terms, i.e. any terms involving products of flapping angles and, flapping rates, and inflow coefficients

## Slide 13: Rotor Forces and Moments
The normal force term F(1) can be evaluated as:
The in-plane force and torque terms are very large. Will not show here
where

## Slide 14: Rotor Forces and Moments
The inertial forces can be simplified further by removing the terms due to the acceleration of the hub
Simplified forces and moments at the rotor hub:

## Slide 15: Rotor Forces and Moments
Will transform to multi-blade coordinates. E.g. for flapping:
When we sum terms from each blade, we end up with many combinations of sin / cosine function of the azimuth angle:
Recall that the blade azimuths for a four-bladed rotor are related as follows:

## Slide 16: Rotor Forces and Moments
When we evaluate these expressions, many sum to 0
Some sum to a constant:
And other sum to 4/rev harmonics:

## Slide 17: Rotor Forces and Moments
The four-rev harmonics are dominant for vibration, but they have little effect on flight dynamics. Their effect averages to 0 over a rotor revolution, and they can be dropped.
Similar analys can be made for rotor with N blades (rotor will produce N/rev harmonics + steady-state terms)
Forces and moments can be normalized by tip speed and disk area.
Final force and moment coefficients are resolved in hub-wind axes
Introduce rotor solidity parameter

## Slide 18: Rotor Forces and Moments
Thrust: Cz
Roll and pitching moments:

## Slide 19: Rotor Forces and Moments
Longitudinal in-plane force, Cx

## Slide 20: Rotor Forces and Moments
Lateral in-plane force, Cy

## Slide 21: Rotor Forces and Moments
The yaw moment is driven by rotor torque and rotor acceleration

## Slide 22: Rotor Forces and Moments
Final equations require following input
  Aircraft properties
  Control settings
  Flight conditions (aircraft state)
  Rotor states
  Inflow states

## Slide 23: Simplified Expressions for Moments
Torque is can be calculated by the following formula
Uses empirical constants which accounts for non-ideal effects (distorted inflow, tip loss, compressibility)
Can include term to account for increased blade drag at higher thrust coefficients
Induced + Climb Power
Parasite Power
Profile Power

## Slide 24: Simplified Expressions for Moments
Roll and pitch moment of have a dominant term:
The flap frequency can be related to hinge offset and flapping spring:
Final dimensional roll and pitch moment is proportional to flapping angle and “hub moment constant”:
Roll hub moment coefficient
Pitch hub moment Coefficient
Dimensional roll hub moment
Pitch hub moment is similar
Hub moment constant

## Slide 25: Hub Moment
Shear forces at the flapping hinge create moment about hub center
The factor Nb/2 results from averaging over one revolution

## Slide 26: Hub Moment
Roll and pitch moment produced by the main rotor is a combination of (thrust tilt) x (rotor height) + hub moment
For teetering gimballed rotors, the hub moment is 0. All roll and pitch control comes from thrust tilt
For rotors with even a small amount of hinge offset, the hub moment becomes dominant in roll and pitch control authority. Example: UH-60A, 4.7% hinge offset, no flap spring
Roll moment about CG produced by Main Rotor