## Slide 1: Linear Model Analysis
Starting from non-linear EOM in implicit state space
We extract a linearized model usually from numerical linearization

## Slide 2: Linear Model Analysis
Can convert the linearized implicit state space model to an explicit model
Note that we drop the D notation for brevity and boldface vector notation for simplicity
State space matrices must have appropriate dimensions

## Slide 3: Linear Model Analysis
Note, that we can always include the state as an output of the system. Say that y comprises non-state output, then we can augment the output vector with the states
If state derivatives are of interest we can also add them to the output

## Slide 4: HeloSim Simulation Example
HeloSim Model
  24 states (n = 24)
  5 controls (m = 5)
  5 outputs (p = 5)
Will often be interested in state output, so just augment or re-define C and D matrices. For state output, C = I, D = 0 with appropriate dimensions: C = eye(24), D = zeros(24,5)
Airspeed (kts), accelerometers (g), Engine Torque (%)

## Slide 5: HeloSim Simulation Example
Linearized HelSim Model in Hover, Eigenvalues
eig(A)
ans =
0.0000 + 0.0000i
0.0000 + 0.0000i
0.0000 + 0.0000i
0.0000 + 0.0000i
-11.6732 +50.3124i
-11.6732 -50.3124i
-27.2118 + 4.1056i
-27.2118 - 4.1056i
-11.7987 +22.9051i
-11.7987 -22.9051i
-10.6088 + 0.0000i
-3.3007 + 4.9429i
-3.3007 - 4.9429i
-5.1593 + 0.0000i
-1.5511 + 0.0000i
0.2732 + 0.5476i
0.2732 - 0.5476i
-0.1121 + 0.5683i
-0.1121 - 0.5683i
-0.6618 + 0.0000i
-0.1639 + 0.0000i
-0.1034 + 0.0000i
-0.5631 + 0.0000i
-11.6279 + 0.0000i
0 Eigenvalues
High Frequency Eigenvalues
due mainly to rotor and inflow modes
Low Frequency Eigenvalues
due main body response
Note the unstable mode

## Slide 6: HeloSim Simulation Example

## Slide 7: HeloSim Simulation Example
Linearized HelSim Model in Hover, Control Matrix
B =
-2.9469e-02 -1.0214e-01 5.3367e-02 3.4107e-02 0
5.4920e-02 -5.4958e-02 -5.6629e-03 -3.3383e-02 0
-1.5401e-03 -5.3997e-03 -1.2198e+00 2.0633e-02 0
4.7582e-02 -1.8732e-01 1.9991e-02 3.3048e-02 0
1.3045e-02 1.1495e-02 2.2998e-03 4.6259e-03 0
2.9484e-03 -1.0643e-02 3.3611e-02 2.4487e-02 0
0 0 0 0 0
0 0 0 0 0
0 0 0 0 0
0 0 0 0 0
0 0 0 0 0
0 0 0 0 0
0 0 0 0 0
0 0 0 0 0
0 0 0 0 0
-6.1226e-06 6.7317e-05 1.9755e+00 -2.2479e-05 0
-2.8923e-01 3.4939e+00 -4.8300e-01 -1.1976e+00 0
-1.9667e+00 -6.1847e-01 4.1666e-01 2.1491e-01 0
-2.0042e-08 2.2036e-07 5.5773e-03 -7.3585e-08 0
-3.4400e-03 3.7479e-02 -5.5094e-03 -1.2516e-02 0
-2.0125e-02 -6.4064e-03 4.3710e-03 2.1393e-03 0
1.5379e-06 -6.1066e-06 -2.3185e-01 1.3317e-02 0
0 0 0 0 6.6914e+03
0 0 0 0 4.1708e+03

## Slide 8: Linear Model Analysis
Linear models can be analyzed in MATLAB using LTI tools (in control system toolbox).
First construct state space LTI object:
sys=ss(A,B,C,D); %sys = LTI object representing the linear system
Can then analyze using a variety of LTI tools (examples):
eig(sys); %Eigenvalues of system (equivalent to eig(A))
tzero(sys); %Transmission zeros of system (MIMO transmission zeros)
pzmap(sys); %Plots zeros and eigenvalues on complex plain
Can generate responses, by default these plot response for every combination of input / output (m x p plots)
step(sys); %Unit step response
impulse(sys); % Unit impulse response
bode(sys); %Frequency response (magnitude and phase versus frequency)
initial(sys,x0); %Response to initial conditions defined by state vector x0
Any operation with sys(i,j) will isolate results for single input j to single output i
Can use output arguments to pull out data rather than generate plot.
e.g. [y,t,x]=step(sys) %returns outputs, time, and states for unit step response
Can also get transfer function and zero-pole-gain form of system:
sys_tf(sys); sys_zpk=zpk(sys); %Provided MIMO Transfer function in polynomial or factored form

## Slide 9: Theory of LTI models

## Slide 10: Theory of LTI models

## Slide 11: Theory of LTI models

## Slide 12: Theory of LTI models
For most linear models of aircraft, any repeated eigenvalues are often associated with modes that can be de-coupled from the aircraft model.
Very often these repeated eigenvalues are at the origin of the complex plane (l = 0) and associated with simple integration of states, e.g.
In some cases, there may be repeated eigenvalues associated with an aircraft component that is replicated multiple times (e.g. same actuator properties used for multiple surfaces):
In these cases, the repeated eigenvalues with multiplicity m usually have m distinct eigenvectors (the “fully degenerate case”). In those cases, the A matrix is still diagonalizable.
It would be extremely rare for any of the fundamental modes of the aircraft dynamics to have repeated eigenvalues.
Linear Aircraft Dynamics

## Slide 13: Theory of LTI models
Assuming fully diagonalizable system:
As discussed earlier, V is constructed form the eigenvectors. It can also be shown that V-1 is constructed from the “left eigenvectors”:

## Slide 14: Theory of LTI systems
The LTI system response is now de-composed into a summation of responses of each mode:
Note the scalar terms within the summations are multiplied by the eigenvector, these break out the modal responses
Forced Response
Response to Initial Conditions
Scalar terms govern shape of time response
Eigenvectors govern relative magnitude and phase of each state

## Slide 15: Theory of LTI systems
For now focus on response to ICs. Individual mode responses are of the form:
Note that when we sum all the modes together, it must be true that the value of x(t=0) matches our initial condition.
If li is a real number, then vi and wi are real vectors. The initial state vector is always real (clearly, since it represents physical values). The modal response can then be written as:

## Slide 16: Real Eigenvalues
For real eigenvalues, the mode response of each state is simply an exponential function:
Response of kth state component

## Slide 17: Complex Eigenvalues
Complex eigenvalues always come in conjugate pairs, and their eigenvectors are also conjugate pairs
Pairs of complex eigenvalues combine to form a product of a sinusoidal function and an exponential function.
Note that all imaginary numbers vanish in the state response (this has to be the case, since the states are physical values)
For the given mode, all states respond with the same frequency w and damping s, but different amplitude A and phase 

## Slide 18: Complex Eigenvalues
Complex eigenvalues result in damped, divergent, or neutrally stable oscillations
Response of kth state component

## Slide 19: Total State Response
Total state response is a sum of all of the modes
Example:

## Slide 20: Total State Response
Can find that imaginary terms drop out
Can now plot individual modes and show how they sum to total system response.
Can also show how eigenvectors govern relative magnitude and phase of the response.

## Slide 21: Response of Example System

## Slide 22: Important Properties of Eigenvalues
Eigenvalues tell us if a mode is stable or unstable:
Eigenvalues tell us the rate of subsidence or divergence, e.g. the time to half amplitude or time to double amplitude:
Eigenvalues tell us the frequency and period of oscillation of oscillatory modes:

## Slide 23: Important Properties Eigenvectors
Eigenvectors tell us the relative magnitude of the response observed in each state for a given mode. Note that eigenvectors have the same dimension as the state, and each component corresponds to the various states (in same order as with the state vector).
Therefore the eigenvector has units – the same units as the state vector. Important to understand the difference between units of each state when analyzing the eigenvector.
Eigenvectors tell us the relative phase of the response of each state if the mode is oscillatory (complex), e.g.:

## Slide 24: Important Properties Eigenvectors
Continue example:
Note that frequency and rate of subsidence are the same for both states. But the signals are 180° out of phase and the magnitude of the blue line is 5 x that of the red.

## Slide 25: Forced Response
So far, we have focused on response to initial conditions. Can also looked at the forced response due to input:
The forced response of each mode is actually a convolution of the state transition matrix and a function proportional to the input signals:
The convolution integral cannot be evaluated analytically except for very simple input signals. However, it tells us that the forced response will contain a transient response due to the modes and a steady-state response due to the input signal:

## Slide 26: Isolation of Modal Responses
In general, all modes will appear in the state response. However, there are special cases where certain modes will not appear in either the response to initial conditions or the forced response.
For initial conditions:
In simulation, it is possible to select initial conditions that isolate the response of a single mode. For a mode with a real eigenvalue just set the initial state vector to a multiple of the eigenvector. For a mode with complex eigenvalues, set the initial state vector to a multiple of the real part of the eigenvectors.

## Slide 27: Isolation of Modal Response
Generally, not possible to isolate a mode using an input signal (forced response).
This would require:
This is only possible if the aircraft is not under-actuated (the number of controls is at least equal to the number of states). This is very unusual.
However, in practice we can find input signals that tend to excite some modes much more than others.
This is needed in flight test, since we cannot “set initial conditions” in actual flight.