## Slide 1: Stability and Control Derivative Models
In previous lecture we derived the 8-state linear model
Implies that the dynamics are based only on the rigid body equations of motion. The rotor states respond instantaneously to controls and state perturbations, resulting in instantaneous changes and forces and moments from the rotor system
Consider the rigid body equation of motion for u:
This equation linearizes to the following:
In this equation, the subscript e denotes the equilibrium value of the state. In the last term we take a gradients of the aero force term with both the state and control vectors.
Note that I have gone back to using boldface for vectors and the D symbol to indicate perturbation states. This is required for clarity in the derivation below.

## Slide 2: Stability and Control Derivative Models
The gradients return a row vector with partial derivatives of the force with each state and control. We can write the state terms as:
The terms in the row vector are the stability derivatives. We use a shorthand notation of the following form:
The subscript e indicates the derivatives are evaluated at the equilibrium flight condition. Thus, the resulting stability derivatives become constant numerical values for a given flight condition.
Note that these are “mass normalized” derivatives. In some texts (e.g. Etkin and Reid) they use the same symbol for S&C derivatives that are non mass normalized. As a result the units are different in those texts.

## Slide 3: Stability and Control Derivative Models
We can write the control gradient term as
The terms in the row vector are the control derivatives. We use a shorthand notation of the following form:
Note that the stability derivatives with respect to the Euler angles are typically 0. At least in out-of-ground effect (OGE) flight the aircraft attitude does not affect aero forces and moments on the aircraft)
In-ground-effect (IGE), there can be some influence of aircraft attitude (and also altitude) on the aero forces and moments.
If we linearize the helicopter in a rectilinear trim flight condition, then the trim value of the angular rates will be 0. This will eliminate some of the inertial terms:

## Slide 4: Stability and Control Derivative Models
The resulting linear model matrices:

## Slide 5: Stability and Control Derivative Models
The moment terms are normalized by the corresponding moments of inertia:
For roll and yaw there is cross-coupling from the product of inertia, and we define the coupled lateral-directional derivatives (denoted with the “prime” symbol):
Note that the coupled lateral-directional derivatives reduce to the simple derivatives when the product of inertia is 0 (Ixz = 0)

## Slide 6: Stability and Control Derivatives
Note that the system matrix contains stability derivatives, inertial terms, gravity terms, and kinematic terms. Below I have color coded the terms so you can identify them.
The control matrix (B) consists entirely of the control derivatives.
The gravity and inertial terms are deterministic if one knows the trim and the mass properties of the aircraft.
Therefore, we can back out the predicted S&C derivatives from the 8-state linear model generated by our simulation.

## Slide 7: Stability and Control Derivative Models
Consider UH-60 simulation, trimmed at 120 knots forward airspeed.
Trim model with forward speed of 202.6 ft/sec
We can get trim states from x0 using: x0(1:8)
Note that I ran a zero bank angle trim (ay = 0)
Now lets look at the A matrix for the 8-state model:
Can start to see how values correlate with the theoretical state space model and to pull out S&C derivatives
Ar =
-0.0391 0.0089 0.0416 -1.1797 5.1837 14.7030 0 -32.1639
0.0014 -0.1432 -0.0123 -5.9103 -0.6508 -200.4152 32.1639 0.0000
0.0142 -0.0336 -0.8565 -14.5575 203.1310 -0.4156 0 0.6249
0.0032 -0.0321 0.0114 -4.2568 -1.3415 0.5894 0 0
0.0001 0.0065 -0.0064 0.4700 -1.6919 -0.1467 0 0
-0.0031 0.0135 0.0096 -0.1872 -0.1652 -0.6384 0 0
0 0 0 1.0000 -0.0000 -0.0194 -0.0000 0.0000
0 0 0 0 1.0000 -0.0000 -0.0000 0

## Slide 8: Stability and Control Derivatives
In the previous slide we can find that the kinematic and gravitation terms are exact
For several terms the stability derivative is simply identical to an element of A, e.g.:
For other terms, you need to remove the inertial effect to get the true value of the stability derivative, e.g. (note that you can lose precision here):
The control derivatives, can simple be taken directly form the B matrix

## Slide 9: Stability and Control Derivative Models
Note: You cannot get the classic S&C derivatives directly from the full order model! If you try this, you will get completely wrong results!
As example, lets look at the upper left quadrant of the full order A matrix in hover and try to extract the roll damping derivative:
Now let’s look at the full order B matrix and try to pull out the roll control moment derivative:
If you look at the reduced order model, the same values are:
These are obviously very different. Why?
In the full order model, many of the important stability and control effects come through the rotor, and require a change in rotor state (e.g. the lateral flapping angle changes to induce the roll damping and roll control derivatives effects from the main rotor). The effects are still present in the full order model, but involve multiple states.

## Slide 10: Stability and Control Derivative Models
It is often desirable to change the state order in order to partition the system into lateral-directional dynamics, longitudinal dynamics, and cross-coupling effects:
The modified state space matrices will be of the form:
The new matrices contain sub-matrices representing the lateral on-axis effects, longitudinal on-axis effects, lateral-to-longitudinal cross-coupling effects, and longitudinal-to-lateral cross coupling effects.
The terms are exactly the same as those in the matrices presented on slide 4 but simply rearranged to new (row, column) locations
In MATLAB we can re-order the matrices using the following:
Longitudinal States
Longitudinal Controls
Lat.-Dir. States
Lat.-Dir. Controls
Ar=Ar([1 3 5 8 2 4 6 7], [1 3 5 8 2 4 6 7]);
Br=Br([1 3 5 8 2 4 6 7], [2 3 1 4]);

## Slide 11: Stability and Control Derivative Models
Lets look at the resulting system with re-order states:
Ar =
-0.0261 0.0163 2.1589 -32.1526 -0.0307 -1.3456 -0.0235 0
0.0111 -0.3477 0.2881 -1.0558 0.0068 -0.1030 -0.1796 1.5691
0.0109 0.0036 -0.8136 0 0.0149 0.2036 -0.0681 0
0 0 0.9988 0 0 0 0.0488 0.0000
0.0145 -0.0049 -1.4953 0.0516 -0.0638 -2.2907 0.4516 32.1143
0.0495 -0.0010 -2.0971 0 -0.0229 -6.2936 0.2772 0
0.0047 0.0042 -0.1568 0 0.0046 -0.3159 -0.1892 0
0 0 -0.0016 -0.0000 0 1.0000 0.0328 -0.0000
Br =
-0.1705 0.0516 0.0038 0.0580
-0.0102 -0.7932 0.0001 0.0221
0.0378 -0.0026 -0.0007 -0.0046
0 0 0 0
0.0176 -0.0094 0.0922 -0.0577
0.0395 -0.0263 0.1650 -0.0448
0.0022 0.0201 0.0096 0.0198
0 0 0 0
Blue = Longitudinal
Red = Lateral-Directional
Green = Cross-Coupling
u w q q v p r f
We can see there is substantial cross-coupling in helicopter dynamics
Nonetheless, we will be interested in simplifying more by breaking out de-coupled longitudinal and lateral-directional dynamics

## Slide 12: Stability and Control Derivative Models
Longitudinal Model
Lateral-Directional Model
In some cases we can also make assume the trim attitude angles are small:

## Slide 13: Stability and Control Derivative Models
Go back to the complete 8 state model (before reordering the states), and focus on the diagonal terms and on-axis control terms:
You will find that the diagonal terms in A are usually negative (especially in rows 3-6 corresponding to w, p, q, and r). These are damping derivatives. They produce a force or moment in the opposite direction of the state change.
The highlighted control derivatives represent the intended force or moment change produced by each control axis
Consider the hover linear model and compare eigenvalues to the damping derivatives in circled in blue above

## Slide 14: Stability and Control Derivative Models
Eigenvalues of reduced order hover model compared to damping derivatives:
-6.2078 + 0.0000i => Roll Subsidence Mode
-1.3316 + 0.0000i => Pitch Subsidence Mode
0.2798 + 0.5500i
0.2798 - 0.5500i
-0.1190 + 0.5635i
-0.1190 - 0.5635i
-0.3425 + 0.0000i => Heave Subsidence Mode
-0.1736 + 0.0000i => Yaw Subsidence Mode
We find the damping derivatives are generally pretty close to the eigenvalue for the subsidence mode associated with the same degree of freedom. The one exception in this case is the pitch damping which is 39% off, but the others are all within 10%.
One generally finds that the damping derivative alone is a reasonable approximation for the subsidence mode in hover and low speed.
The roll damping derivative usually continues to be a good approximation of the roll subsidence mode into high speed forward flight.

## Slide 15: Stability and Control Derivative Models
We can derive very simple, first order models of each control axis using only the damping derivative and the on-axis control derivative:
These models are crude and generally only good for modelling the short-term time response, and a narrow range of frequencies in the frequency response
However, the frequency range where they are reasonably accurate is the same frequency range that a pilot typically operates in (1-10 rad/sec), and thus these models are useful for understanding rotorcraft handling qualities