## Slide 1: Hover Flight Dynamics
Will investigate hover dynamics using the HeloSim UH-60 model as an example
Will leverage simplified de-coupled longitudinal / lateral dynamics so we can relate the dynamics directly to specific S&C derivatives
Will find that these simplified models are not necessarily very accurate, but they still give some physical insight on the dynamics
Later we will upgrade the dynamic models to improve matching with full order models
Note that the hover dynamics are really dominated by the main rotor and the tail rotor. The airframe aerodynamics have a small effect as the dynamic pressure is by definition very small, so lift and drag forces on the airframe components have only a small impact in hover.

## Slide 2: Simplified Longitudinal Dynamics in Hover
Start with our de-coupled linear model of longitudinal dynamics, with small angle assumption. In hover, the equilibrium velocities are obviously 0, so those terms can be eliminated:

## Slide 3: Longitudinal S&C Derivatives
Look at the S&C derivatives, what contributes to them physically and their relative importance.
Start with the important stability derivatives:
  Xu : As airspeed increases or decreases, the rotor will tend to experience longitudinal flapping (“rotor blow back”) such that the tilt of the rotor tip path plane generates a force in the opposite direction of the velocity
  Mu : The “rotor blow back” described above will also generating a pitching moment which will tend to pitch the aircraft nose up when it starts to move forward and nose down with rearward motion
  Mq : This is the pitch damping derivative. If the aircraft begins to rotate nose up or nose down, the gyroscopic precession of the rotor will cause longitudinal flapping that generates a moment that tends to resist the rotation
  Zw : Heave damping: If the aircraft translates up or down it changes the inflow to the main rotor, which will change the rotor thrust in such a way that it resists this motion

## Slide 4: Longitudinal S&C Derivatives
Control derivatives:
  Xd long : A longitudinal cyclic input will cause longitudinal flapping that generates forward or aft force
  Md long : This is the primary longitudinal control derivative. The flapping described above will likewise generate a pitching moment.
  Zd coll : This is the primary collective control derivative. Changes in collective pitch will change the rotor thrust.
Long. Cyclic Applied
Hub Moment
Moment about CG = DM
DX

## Slide 5: Simplified Longitudinal Dynamics in Hover
The following S&C derivatives can be neglected with a reasonable level of accuracy in hover (but not necessarily in forward flight)
  Xw, Zd long, Xd coll : These values are generally very small in hover.
  Xq, Zq : You will find that these derivatives are not actually “small”. But we know from experience they have little impact on hover dynamics.
  Mw, Md coll : These derivatives can be non-zero if the rotor is longitudinally offset from the CG, but they have little importance in hover (note that Mw, becomes very significant in forward flight)
  Zu : As airspeed increases or decreases, the rotor thrust will tend to increase due to the “translational lift effect”, i.e. the reduction of induced inflow with forward airspeed. But the thrust always increases when translating away from hover, no matter what direction the aircraft flies! So the linearization of this effect comes to 0.
u
Z
Linearize Here in Hover:
dZ/du = 0

## Slide 6: Simplified Longitudinal Dynamics in Hover
With neglected S&C derivatives removed:
We find that the longitudinal translation / pitch dynamics (u , q, q, dlong) become decoupled from the vertical dynamics (w , dcoll). Can separate into decoupled 1st order and 3rd order linear models.
First order vertical dynamics (or “heave dynamics”):
3rd order longitudinal dynamics:

## Slide 7: Heave Dynamics
A simple 1st order system. Can be represented by a transfer function as well:
The step response to a collective input can be written in the closed form solution:
If the heave damping derivative is negative these dynamics will always be stable:
The collective control axis is a “Vertical Speed Command Response”. The control sensitivity is driven by the ratio of the control derivative over the damping derivative:
Step Input
Step Response
Heave time constant

## Slide 8: Heave Dynamics
If the damping derivative is too low, the sensitivity is high, but the time constant is long. This generally results in poor handling qualities. Larger time constant will feel like a “Vertical Acceleration Command Response” instead of Vertical Speed Command. On the other hand, if the damping is too high, the control sensitivity in the vertical axis can be too low
Sample 1st order response using UH-60 heave axis derivatives + reponse with half and double the actual damping derivative:

## Slide 9: Longitudinal Dynamics
We can apply Laplace Transform analysis to the 3rd order longitudinal dynamics as well:
Take Laplace Transform
Invert Matrix

## Slide 10: Longitudinal Dynamics
Stability of the longitudinal response is governed by a 3rd order characteristic equation. The “hover cubic”:
Cannot get closed form solution for these roots, but we can use the Routh-Hurwitz criterion to determine if the dynamics are stable
Consider 3rd order polynomial:
The RH Criterion necessary condition for stability is that all coefficients of the polynomial must be the same sign. This implies that they are all positive (since the first coefficient is 1):
Note: The expression only includes stability derivatives (no control derivatives)

## Slide 11: Longitudinal Dynamics
The sufficient condition for stability for a third order system is
We can summarize stability requirements in terms of the stability derivatives:
The last criteria is often not met. The term on the right side is usually positive (again because the damping derivatives are <0), but the Mu derivative is often too large to meet this requirement.
These are typically met since these damping derivatives are usually < 0
This is typically met because usually Mu > 0
?

## Slide 12: Longitudinal Dynamics
Physical analogy of the longitudinal hover phugoid mode – think of a moving cart with the helicopter attached to the cart and free to pivot about its CG
The Mq and Xu derivatives provide damping to the system, but the Mu derivative can add energy, leading to instability if it is too large

## Slide 13: Hover Longitudinal Dynamics of HeloSim UH-60
Extract the 4 state longitudinal model of UH-60:
Can see the unstable phugoid, pitch subsidence, and heave subsidence modes (somewhat different from full order model, but similar)
A good way to see the de-coupling of the heave dynamics and the longitudinal dynamics is to look at the transfer functions for particular input / output pairs.
If we show certain transfer functions in zero-pole-gain (zpk) form, then we can see approximate pole-zero cancellations. This is the mathematical equivalent of approximate de-coupling
Along =
-0.0261 0.0163 2.1589 -32.1526
0.0111 -0.3477 0.2881 -1.0558
0.0109 0.0036 -0.8136 0
0 0 0.9988 0
eig(Along)
-1.1230 + 0.0000i
0.1420 + 0.5431i
0.1420 - 0.5431i
-0.3482 + 0.0000i
Pitch Subsidence
Unstable Hover Phugoid
Heave Subsidence

## Slide 14: Hover Longitudinal Dynamics of HeloSim UH-60
LTI system for longitudinal dynamics:
Get zpk form of the vertical velocity response to collective:
We can see the approximate pole zero cancellations. Can use the minreal function (minimum realization) to extract this in MATLAB. Need to use a tolerance for the approximate pole zero cancellations.
syslong=ss(Along,Blong,eye(4),zeros(4,2));
sys_wdcol=syslong(2,2);
sys_wdcol=zpk(sys_wdcol)
sys_wdcol =
-0.79323 (s+1.123) (s^2 - 0.2829s + 0.3112)
---------------------------------------------
(s+1.123) (s+0.3482) (s^2 - 0.2839s + 0.3151)
Extracts system from input 2 to output 2
Converts to zero-pole-gain transfer function
minreal(sys_wdcol,0.01)
-0.79323
----------
(s+0.3482)

## Slide 15: Hover Longitudinal Dynamics of HeloSim UH-60
Now do a similar process for longitudinal velocity response to longitudinal input:
Again we see approximate pole-zero cancellation, this time the heave subsidence mode is cancelled and we are left with thw pitch subsidence and phugoid modes:
Now we will move on to lateral-directional dynamics. In hover, the lateral / directional dynamics have a lot of analogies to longitudinal / vertical dynamics
sys_udlong =syslong(1,1);
sys_udlong = zpk(sys_udlong)
-0.17048 (s+0.3478) (s^2 + 0.3362s + 7.112)
---------------------------------------------
(s+1.123) (s+0.3482) (s^2 - 0.2839s + 0.3151)
sys_udlong = minreal(sys_udlong,0.01)
-0.17048 (s^2 + 0.3362s + 7.112)
----------------------------------
(s+1.123) (s^2 - 0.2839s + 0.3151)

## Slide 16: Simplified Lateral-Dir. Dynamics in Hover
Start with our de-coupled linear model of lat.-dir. dynamics, with small angle assumption. In hover, the equilibrium velocities are obviously 0, so those terms can be eliminated:
An important thing to remember about hover – the main rotor system is axis-symmetric. So it will behave the same way in sideward translation and roll as it does in longitudinal translation and pitch.
Recall we had a hub-wind axis transformation for the main rotor model, such that the same equations could be used with the local in plane velocity coming from any direction
So we will see a lot of analogous behavior in lateral dynamics with a few key differences
  The sign convention is different – positive roll attitude causes positive lateral velocity, whereas it is the opposite with pitch and longitudinal velocity. There is no difference in physics here, but in the equations some of the key terms have different signs
  The tail rotor has significant effects in hover and causes some differences.
  The moments of inertia are often quite different in roll compared to pitch. For example on UH-60, the roll inertia is order of magnitude smaller than pitch inertia. This is conventional for conventional helicopters. For tilt-rotors it can be very different – roll inertia is often the largest

## Slide 17: Simplified Lat.-Dir. Dynamics in Hover
Now lets summarize the S&C derivatives, what contributes to them physically and their relative importance. We will start with the important stability derivatives:
  Yv : Analogous to Xu, as lateral airspeed increases or decreases, the rotor will tend to flap laterally (“rotor blow back”) generating a force in the opposite direction
  Lv : The “rotor blow back” described above will also generating a rolling moment which will tend to roll the aircraft left when it starts to move to the right. This term is analogous to Mu , but because of differences in sign convention this the value is negative instead of positive
  Lp : Roll damping, analogous to Mq
  Nr : Yaw damping, this comes mainly form the tail rotor, tends to resist rotations in yaw
Important control derivatives:
  Yd lat , Ld lat , Nd ped : These are primary control derivative, very much analogous to the control derivatives kept in the longitudinal case
The following S&C derivatives can be neglected with a reasonable level of accuracy in the hover flight condition:
  Nv : It is a fairly rough approximation to neglect this term. This is the directional stability term that will arise due to changes in inflow of the tail rotor in sideward flight. It will tend to have a positive value such that it turns the aircraft into the relative air flow. However, we will neglect it to simplify hover dynamics.
  Yr , Yp, Lr, Np : These are relatively small stability derivatives that have little impact on hover dynamics.
  Yd ped, Ld ped : These terms have a significant value (due lateral force from the tail rotor), but they can be neglected to simplify hover dynamics.
  Nd lat : Not usually a significant control derivative

## Slide 18: Simplified Lat.-Dir. Dynamics in Hover
With neglected S&C derivatives removed:
Once again it is decoupled into a 1st order and a 3rd order linear model.
First order yaw dynamics:
3rd order lateral dynamics (dropping “prime” notation):

## Slide 19: Lateral-Directional Analysis
Yaw dynamics are first order, and analogous to heave (rotation about vertical axis instead of translation). Time constant and control sensitivity are directly related to yaw damping and the control derivative
Lateral dynamics are very much analogous to the longitudinal dynamics. The dynamics result in a roll subsidence mode and a lateral phugoid. Note that there different sign conventions in lateral dynamics, e.g. positive roll leads to positive to lateral velocity (where as positive pitch leads to negative longitudinal velocity). This is reflected in the sign of the gravity term. So note the sign differences below:
Can apply Routh-Hurwitz again to find criteria for stability

## Slide 20: Lateral-Directional Analysis
We can summarize stability requirements:
In the case of the lateral-directional dynamics, the last criteria is sometimes met, but sometimes not. For most helicopters, the roll inertia is significantly lower than the pitch inertia. As a result, the roll damping is a lot larger than the pitch damping. This causes the term on the right to be more negative than the term on the left. This is the case for the UH-60. However, it is configuration dependent.
These are typically met since these damping derivatives are usually < 0
This is typically met because usually Lv < 0
Note that Lv < 0, and this criterion is stipulating that Lv cannot be too negative